## Slide 1: Compute Shaders Optimize your engine using compute
Lou Kramer
Developer technology Engineer, AMD
Organized by

## Slide 2: Agenda
Compute shaders – What are they?
Execution model
Programming
Example: Downsampling using compute
Lou Kramer // 4C Prague // 2018.10.05

## Slide 3: Compute shaders – what are they?
… and what makes them different from e.g. pixel shaders?
Lou Kramer // 4C Prague // 2018.10.05
Tessellation
Pre-Fragment
Post-Fragment
Rasterizer
Color Blending
Input Assembler
Vertex Shader
Geometry Shader
Pixel Shader
Compute Shader
?

## Slide 4: On the hardware-side
Lou Kramer // 4C Prague // 2018.10.05
Graphics Processor
Rasterizer
Compute Unit
Render Backend
Command buffers
Draw() …
Compute Unit
Compute Unit
…
…
Compute Unit
Command Processor

## Slide 5: On the hardware-side
Lou Kramer // 4C Prague // 2018.10.05
Command Processor
Graphics Processor
Rasterizer
Compute Unit
Render Backend
Command buffers
Dispatch() …
Compute Unit
Compute Unit
…
…
Compute Unit

## Slide 6: On the hardware-side
Lou Kramer // 4C Prague // 2018.10.05
Command Processor
Graphics Processor
Rasterizer
Compute Unit
Render Backend
Command buffers
Dispatch() …
Compute Unit
Compute Unit
…
…
Compute Unit
Input: constants and resources
Output: writable resources (UAVs)

## Slide 7: And on the code-side?
Creating the compute pipeline requires less information than creating the graphics pipeline:
Lou Kramer // 4C Prague // 2018.10.05
Graphics pipeline | Compute pipeline
One to several shader stages (VS, HS, DS, GS, PS) Input assembler Tessellation Rasterizer … | CS shader stage

## Slide 8: Short summary 
Compute shader introduce less hardware overhead compared to the other shader stages
Lou Kramer // 4C Prague // 2018.10.05

## Slide 9: Execution model

## Slide 10: Execution model of shaders
GPUs are designed to process a massive amount of data in parallel
Need to run the same program on
  Many vertices
  Many pixels
Lou Kramer // 4C Prague // 2018.10.05
One shader for many pixels

## Slide 11: Execution model of shaders
GPUs are designed to process a massive amount of data in parallel
Need to run the same program on
  Many vertices
  Many pixels
Lou Kramer // 4C Prague // 2018.10.05
The smallest work item for compute shaders is called a thread

## Slide 12: Execution model of shaders
GPUs are designed to process a massive amount of data in parallel
Need to run the same program on
  Many vertices
  Many pixels
In hardware, the parallelism is realized using
  SIMD units, which are grouped on a compute unit (SIMD – Single Instruction Multiple Data)
  Many compute units
Lou Kramer // 4C Prague // 2018.10.05
The smallest work item for compute shaders is called a thread

## Slide 13: GCN Architecture: compute unit
Scheduler
Vector registers 64KiB
Local Data Share 64KiB
L1
16KiB
Texture Units
Branch & Message unit
Vector units (4x SIMD-16)
Scalar unit
Scalar registers (12.5KiB)

## Slide 14
Lou Kramer // 4C Prague // 2018.10.05
Graphics Processor
Rasterizer
Compute Unit
Render Backend
Command buffers
Draw() …
Compute Unit
Compute Unit
…
…
Compute Unit
Command Processor

## Slide 15
Lou Kramer // 4C Prague // 2018.10.05
Graphics Processor
Rasterizer
Render Backend
Command buffers
Draw() …
…
…
Command Processor
For example:
A Vega 64 has 64 compute units!

## Slide 16: Hierarchy of work items
Lou Kramer // 4C Prague // 2018.10.05
0,0,0
0,0,0
0,0,0
0,0,1
0,0,0
0,0,0
0,0,0
0,2,1
0,0,0
1,0,0
2,0,0
3,0,0
0,1,0
2,1,0
0,2,0
X (dim 0)
Y (dim 1)
Z (dim 2)
Dispatch(4,3,2);
The dispatch call invokes 4 * 3 * 2 = 24 thread groups
in undefined order
based on: https://docs.microsoft.com/en-us/windows/desktop/direct3dhlsl/sv-dispatchthreadid

## Slide 17: Hierarchy of work items
Lou Kramer // 4C Prague // 2018.10.05
0,0,0
0,0,0
0,0,0
0,0,1
0,0,0
0,0,0
0,0,0
0,2,1
0,0,0
1,0,0
2,0,0
3,0,0
0,1,0
2,1,0
0,2,0
X (dim 0)
Y (dim 1)
Z (dim 2)
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,3
0,1,3
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,2
0,1,2
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,1
0,1,1
0,0,0
1,0,0
2,0,0
3,0,0
4,0,0
5,0,0
6,0,0
7,0,0
0,1,0
5,1,0
Thread group (2,1,0)
In the compute shader,
the thread group size is declared using
[numthreads(8, 2, 4)]
-> each thread group has 64 threads
Dispatch(4,3,2);
The dispatch call invokes 4 * 3 * 2 = 24 thread groups
in undefined order
based on: https://docs.microsoft.com/en-us/windows/desktop/direct3dhlsl/sv-dispatchthreadid

## Slide 18: Hierarchy of work items
Lou Kramer // 4C Prague // 2018.10.05
0,0,0
0,0,0
0,0,0
0,0,1
0,0,0
0,0,0
0,0,0
0,2,1
0,0,0
1,0,0
2,0,0
3,0,0
0,1,0
2,1,0
0,2,0
X (dim 0)
Y (dim 1)
Z (dim 2)
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,3
0,1,3
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,2
0,1,2
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,1
0,1,1
0,0,0
1,0,0
2,0,0
3,0,0
4,0,0
5,0,0
6,0,0
7,0,0
0,1,0
5,1,0
Thread group (2,1,0)
In the compute shader,
the thread group size is declared using
[numthreads(8, 2, 4)]
-> each thread group has 64 threads
Thread (5,1,0)
SV_GroupThreadID: (5,1,0)
SV_GroupID: (2,1,0)
SV_DispatchThreadID: (2,1,0) * (8,2,4) + (5,1,0) = (21, 3, 0)
SV_GroupIndex: 0 * 8 * 2 + 1 * 8 + 5 = 13
Dispatch(4,3,2);
The dispatch call invokes 4 * 3 * 2 = 24 thread groups
in undefined order
based on: https://docs.microsoft.com/en-us/windows/desktop/direct3dhlsl/sv-dispatchthreadid

## Slide 19: Hardware: scheduling work
Lou Kramer // 4C Prague // 2018.10.05
0,0,0
0,0,0
0,0,0
0,0,1
0,0,0
0,0,0
0,0,0
0,2,1
0,0,0
1,0,0
2,0,0
3,0,0
0,1,0
2,1,0
0,2,0
X (dim 0)
Y (dim 1)
Z (dim 2)
…
…
Each thread group gets scheduled to an available compute unit
Dispatch(4,3,2);
The dispatch call invokes 4 * 3 * 2 = 24 thread groups
in undefined order

## Slide 20: Hardware: scheduling work
Lou Kramer // 4C Prague // 2018.10.05
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,3
0,1,3
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,2
0,1,2
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,1
0,1,1
0,0,0
1,0,0
2,0,0
3,0,0
4,0,0
5,0,0
6,0,0
7,0,0
0,1,0
5,1,0
Thread group (2,1,0)
In the compute shader,
the thread group size is declared using
[numthreads(8, 2, 4)]
-> each thread group has 64 threads
Scheduler
The threads get scheduled to the SIMDs

## Slide 21: Hardware: scheduling work
Lou Kramer // 4C Prague // 2018.10.05
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,3
0,1,3
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,2
0,1,2
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,1
0,1,1
0,0,0
1,0,0
2,0,0
3,0,0
4,0,0
5,0,0
6,0,0
7,0,0
0,1,0
5,1,0
Thread group (2,1,0)
In the compute shader,
the thread group size is declared using
[numthreads(8, 2, 4)]
-> each thread group has 64 threads
Threads are scheduled to the SIMD units in bundles
In the case of GCN, the size of such a bundle is 64 and called a wavefront
Per SIMD, several wavefronts can be concurrently in flight

## Slide 22: Hardware: scheduling work
Lou Kramer // 4C Prague // 2018.10.05
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,3
0,1,3
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,2
0,1,2
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,0
0,0,1
0,1,1
0,0,0
1,0,0
2,0,0
3,0,0
4,0,0
5,0,0
6,0,0
7,0,0
0,1,0
5,1,0
Thread group (2,1,0)
In the compute shader,
the thread group size is declared using
[numthreads(8, 2, 4)]
each thread group has 64 threads
Threads are scheduled to the SIMD units in bundles
In the case of GCN, the size of such a bundle is 64 and called a wavefront
Per SIMD, several wavefronts can be concurrently in flight
The whole thread group gets scheduled to a single SIMD unit

## Slide 23: What can we conclude from this?
If thread groups need to communicate with each other, cross compute unit communication is required
Lou Kramer // 4C Prague // 2018.10.05
…
…

## Slide 24: What can we conclude from this?
If thread groups need to communicate with each other, cross compute unit communication is required
Should be kept to a minimum
Lou Kramer // 4C Prague // 2018.10.05
…
…
L2 cache

## Slide 25: What can we conclude from this?
What about threads within a single thread group?
They even have special memory to help: Local Data Share (LDS)
Lou Kramer // 4C Prague // 2018.10.05
Scheduler
Vector registers 64KiB
Local Data Share 64KiB
L1
16KiB
Texture Units
Scalar registers (12.5KiB)

## Slide 26: Local Data Share (LDS)
LDS is also used by other shader stages, e.g. the PS uses it for interpolants
needs to be considered when running async compute & pixel work at the same time
For accessing LDS in the shaders use the groupshared storage-class modifier
Synchronize when doing inter-thread communication
Lou Kramer // 4C Prague // 2018.10.05
groupshared float data[8][8];
[numthreads(8,8,1)]
void main(ivec3 index : SV_GroupThreadID)
{
data[index.x][index.y] = 0.0;
GroupMemoryBarrierWithGroupSync();
data[index.y][index.x] += index.x;
…
}

## Slide 27: Short summary 
Cross thread group / cross compute unit communication
keep to a minimum
Inter-thread communication within a single thread group
there is even special memory to help
Lou Kramer // 4C Prague // 2018.10.05
What about wavefronts?
wavefront wide instructions

## Slide 28: Programming

## Slide 29: Programming
How are instructions executed? Let‘s look at an example
Lou Kramer // 4C Prague // 2018.10.05
groupshared float data[64];
[numthreads(8,8,1)]
void main(uint index : SV_GroupIndex, vec3 groupIndex : SV_GroupID)
{
data[index] = (float4)(0);
GroupMemoryBarrierWithGroupSync();
…
float a = index + b;
int c = groupIndex.x;
…
}
The result of variable a is different
per thread, since it depends on the
thread index
It is a non-uniform variable
Variable c stores the same
value across all threads
It is a uniform variable

## Slide 30: VGPRs & SGPRs
Uniform variables are stored in scalar registers
Require less memory
  a non-uniform variable requires 64 * size_of_variable
  a uniform variable requires 1 * size_of_variable
  even if we have in total more KiB of VGPRs, we can store more uniform variables in the SGPRs
Lou Kramer // 4C Prague // 2018.10.05
Vector registers 64KiB
Local Data Share 64KiB
L1
16KiB
Scalar registers (12.5KiB)
Prefer using uniform variables when possible
VGPRs are precious

## Slide 31: VGPRs & SGPRs
Uniform variables are stored in scalar registers
Require less memory
  a non-uniform variable requires 64 * size_of_variable
  a uniform variable requires 1 * size_of_variable
  even if we have in total more KiB of VGPRs, we can store more uniform variables in the SGPRs
Lou Kramer // 4C Prague // 2018.10.05
Vector registers 64KiB
Local Data Share 64KiB
L1
16KiB
Scalar registers (12.5KiB)
Using too many VGPRs per wavefront can reduce the maximum number of wavefronts per SIMD
Prefer using uniform variables when possible
VGPRs are precious

## Slide 32: Programming
How are instructions executed? Let‘s look at an example
Lou Kramer // 4C Prague // 2018.10.05
groupshared float data[64];
[numthreads(8,8,1)]
void main(uint index : SV_GroupIndex)
{
data[index] = (float4)(0);
GroupMemoryBarrierWithGroupSync();
…
float a = index + b;
…
}
…
v_add_f32 v2, v0, v1
…

## Slide 33: Execution mask
Consider a thread group with 4 threads - [numthreads(4,1,1)]
Lou Kramer // 4C Prague // 2018.10.05
v0
v1
v2
EXEC
0
1
2
3
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
5
7
2
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
6
9
5
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
+
=
+
=
…
v_add_f32 v2, v0, v1
…

## Slide 34: Execution mask
Consider a thread group with 4 threads - [numthreads(4,1,1)]
Remember the SIMD is actually 16-wide?
Lou Kramer // 4C Prague // 2018.10.05
v0
v1
v2
EXEC
0
1
2
3
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
5
7
2
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
6
9
5
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
+
=
+
=
…
v_add_f32 v2, v0, v1
…
Instruction is executed 4 times with each 16 threads – even if EXEC mask is 0

## Slide 35: Execution mask
Consider a thread group with 4 threads - [numthreads(4,1,1)]
Remember the SIMD is actually 16-wide?
Lou Kramer // 4C Prague // 2018.10.05
v0
v1
v2
EXEC
0
1
2
3
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
5
7
2
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
6
9
5
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
+
=
+
=
…
v_add_f32 v2, v0, v1
…
Instruction is executed 4 times with each 16 threads – even if EXEC mask is 0
That‘s the reason why a thread group size of a multiple of 64 is preferable

## Slide 36: Execution Mask - Branches
Lou Kramer // 4C Prague // 2018.10.05
groupshared float data[64];
[numthreads(8,8,1)]
void main(uint index : SV_GroupIndex)
{
…
if (condition)
computeDetail();
else
computeBasic();
…
}
…
block_a:
s_mov_b64 s[0:1], exec
; condition test, writes results to s[2:3]
s_mov_b64 s[2:3], condition
s_mov_b64 exec, s[2:3]
s_branch_execz block_c
block_b:
; ‘if‘ part: computeDetail();
s_not_b64 exec, exec
s_branch_execz block_d
block_c:
; ‘else‘ part: computeBasic();
block_d:
s_mov_b64 exec, s[0:1]
;code afterwards
…

## Slide 37: Execution Mask - Branches
Lou Kramer // 4C Prague // 2018.10.05
A
B
C
D
Save exec
exec = result of test per thread
Invert exec
Restore exec
…
block_a:
s_mov_b64 s[0:1], exec
; condition test, writes results to s[2:3]
s_mov_b64 s[2:3], condition
s_mov_b64 exec, s[2:3]
s_branch_execz block_c
block_b:
; ‘if‘ part: computeDetail();
s_not_b64 exec, exec
s_branch_execz block_d
block_c:
; ‘else‘ part: computeBasic();
block_d:
s_mov_b64 exec, s[0:1]
;code afterwards
…

## Slide 38
s_mov_b64 s[0:1], exec
; condition test, writes results to s[2:3]
s_mov_b64 s[2:3], condition
s_mov_b64 exec, s[2:3]
; ‘if‘ part: computeDetail();
s_not_b64 exec, exec
; ‘else‘ part: computeBasic();
s_mov_b64 exec, s[0:1]
; code afterwards
block_a:
block_b:
block_c:
block_d:
s_branch_execz block_d
s_branch_execz block_c
Lou Kramer // 4C Prague // 2018.10.05

## Slide 39: Execution Mask - Branches
As soon as 1 thread falls into a block
the block gets executed for the whole wavefront
avoid divergent threads within a wavefront
Lou Kramer // 4C Prague // 2018.10.05
groupshared float data[64];
[numthreads(8,8,1)]
void main(uint index : SV_GroupIndex)
{
…
if (condition)
computeDetail();
else
computeBasic();
…
}

## Slide 40: Execution Mask - Branches
As soon as 1 thread falls into a block
the block gets executed for the whole wavefront
avoid divergent threads within a wavefront
Lou Kramer // 4C Prague // 2018.10.05
A
B
C
D

## Slide 41: Execution Mask - Branches
use scalar comparisons when possible if (constant_value < 0) { … }
consider wavefront-wide instructions
Lou Kramer // 4C Prague // 2018.10.05
A
B
C
D
WaveActiveAnyTrue() | Returns exec != 0
WaveActiveAllTrue() | Returns ~exec == 0

## Slide 42: Short summary 
VGPRs are precious
  don‘t use them if you don‘t need to, since it can reduce the maximum number of wavefronts per SIMD
Avoid divergent control flow within a wavefront
  use scalar comparisons when possible if (constant_value < 0) { … }
  consider wavefront-wide instructions
Lou Kramer // 4C Prague // 2018.10.05

## Slide 43: Downsampling

## Slide 44: Downsampling – problem case
Reduce a texture of size 4096x4096 to 1x1
Reduction factor: 2x2 to 1x1
We also want each intermediate level stored -> the mip levels
Lou Kramer // 4C Prague // 2018.10.05
…
4096²
2048²
1024²
1²

## Slide 45: Pixel Shader solution
Each intermediate level is computed in a separate pass, where each level is attached as a new render target
Lou Kramer // 4C Prague // 2018.10.05
2048²
1024²
…

## Slide 46: Pixel Shader solution
Gaps between the sub-levels caused by the barriers and rendertarget decompression
Lou Kramer // 4C Prague // 2018.10.05
…
2048²
1024²

## Slide 47: Pixel Shader solution
Later passes are really tiny and low in occupancy
Lou Kramer // 4C Prague // 2018.10.05
…
2048²
1024²

## Slide 48: Compute shader solution
Pixel shaders can only access the respective pixel in the render target
they don‘t have access to the complete output of the pass
we can‘t combine the computation of several levels in one pass
This is not true for compute shaders
can access each entry of the bound UAVs (unordered access views -> writable resources)
bind all output levels as UAVs
compute all levels in one pass
Lou Kramer // 4C Prague // 2018.10.05

## Slide 49: Compute Shader solution
No barriers between the levels
Constant occupancy over 90% of the time
a performance gain of ~ 100%!
Lou Kramer // 4C Prague // 2018.10.05

## Slide 50: Compute shader solution
Since we want to avoid cross compute unit communication, we let each thread group operate independently on a sub-square of the input texture
Lou Kramer // 4C Prague // 2018.10.05

## Slide 51: Compute shader solution
Since we want to avoid cross compute unit communication, we let each thread group operate independently on a sub-square of the input texture
Lou Kramer // 4C Prague // 2018.10.05
each thread group downsamples as much as possible
e.g. a thread group of 64 threads reduces a 64² square patch down to 1

## Slide 52: Compute shader solution
64²  32²  16²  8²  4²  2²  1
Sub-square of:
4096²  2048²  1024²  512²  256²  128²  64²
Since we want to avoid cross compute unit communication, we let each thread group operate independently on a sub-square of the input texture
Lou Kramer // 4C Prague // 2018.10.05
Once all thread groups are done,
We have a texture with
Texture size = dispatch size

## Slide 53: Compute shader solution
For a 4096² initial texture, this would lead to a Dispatch(64, 64, 1) call
How to downsample the last 64²?
Lou Kramer // 4C Prague // 2018.10.05
Once all thread groups are done,
We have a texture with
Texture size = dispatch size

## Slide 54: Compute shader solution
For a 4096² initial texture, this would lead to a Dispatch(64, 64, 1) call
How to downsample the last 64²?
We need to be sure all thread groups are done
use a global atomic counter (this is cross-compute unit communication!)
The last active thread group will do another round of 64² : 1²
needs to be able to see the actual changes of the other thread groups
bind memory as coherent
this makes sure, the changes are at least visible in L2
and are not ‚stuck‘ in L1
Lou Kramer // 4C Prague // 2018.10.05

## Slide 55: Compute Shader solution
No barriers between the levels
Constant occupancy over 90% of the time
Lou Kramer // 4C Prague // 2018.10.05
This is the last thread group. Not ideal but at least not that long anymore 

## Slide 56: The complete picture
Each thread group performs downsampling on its own 64x64 sub-patch to a 1x1 patch
the last thread group does another round, computing the remaining 6 mip levels
the total number of thread groups is dependent on the initial texture size
a 4096x4096 texture contains 4096 64x64 patches
  Dispatch(64, 64, 1)
  makes a total of 4096 thread groups
Different configurations possible:
  Reduction factor
  Thread group size (64 * N)
  Texture format
Lou Kramer // 4C Prague // 2018.10.05

## Slide 57: The complete picture
Each thread group performs downsampling on its own 64x64 sub-patch to a 1x1 patch
the last thread group does another round, computing the remaining 6 mip levels
the total number of thread groups is dependent on the initial texture size
a 4096x4096 texture contains 4096 64x64 patches
  Dispatch(64, 64, 1)
  makes a total of 4096 thread groups
Different configurations possible:
  Reduction factor
  Thread group size (64 * N)
  Texture format
Lou Kramer // 4C Prague // 2018.10.05
I lied to you before  The above capture was taken with a thread group size of 256!
-> resulted in better cache utility than 64.
But this can vary depending on the specific case!

## Slide 58: Other fun stuff with compute
Various tasks can be solved using compute:
  GeometryFX culls geometry on the GPU
  Particle simulations
  Tiled lights
  Terrain calculations
  Tessellation
  Many post processing effects
  ...
On Vulkan, you can also present on the compute queue
  move the complete post processing work to the compute queue
  already start next frame on the graphics queue
Async compute: overlap compute intensive work with graphics intensive work
  e.g. SSAO & shadow map calculation
Lou Kramer // 4C Prague // 2018.10.05

## Slide 59: Summary
Compute shaders offer nice properties:
  output can be accessed from all threads
  less hardware overhead
  LDS can be used for inter-thread communication within a single thread group
  access to wavefront-wide instructions
For (compute) shaders to be efficient, some guidelines should be kept in mind though:
  keep cross thread group communication to a minimum
  don‘t use VGPRs, if you don‘t need to
  avoid divergent control flow
Lou Kramer // 4C Prague // 2018.10.05

## Slide 60: Lou Kramer
Developer Technology Engineer, AMD
Lou.Kramer@amd.com
lou_auroyup
ANY QUESTIONS?
CONF4C.COM
Organized by

## Slide 61: Special thanks to
Dominik Baumeister
Matthäus Chajdas
Rys Sommefeldt
Steven Tovey
Lou Kramer // 4C Prague // 2018.10.05

## Slide 62: References
https://anteru.net/
https://gpuopen.com/optimizing-gpu-occupancy-resource-usage-large-thread-groups/
https://www.khronos.org/blog/vulkan-subgroup-tutorial
https://docs.microsoft.com/en-us/windows/desktop/direct3dhlsl/sv-dispatchthreadid
Lou Kramer // 4C Prague // 2018.10.05

## Slide 63: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2018 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. Other names are for informational purposes only and may be trademarks of their respective owners.
Lou Kramer // 4C Prague // 2018.10.05

## Slide 64
Lou Kramer // 4C Prague // 2018.10.05

## Slide 65: Lou Kramer
Developer Technology Engineer, AMD
Lou.Kramer@amd.com
lou_auroyup
ANY QUESTIONS?
CONF4C.COM
Organized by